## Slide 1: میکرو کنترلرهای AVR LCD و KeyPad
دانشکده برق و رباتیک
دانشگاه صنعتی شاهرود
حسین خسروی
91-1390

## Slide 2: LCD Interfacing
LCD is finding widespread use replacing LEDs
  The declining prices of LCD
  The ability to display numbers, characters, and graphics
  Incorporation of a refreshing controller into the LCD, thereby relieving the CPU of the task of refreshing the LCD
  Ease of programming for characters and graphics

## Slide 3: LCD Pin out

## Slide 4: LCD Pins Description
Pin | Symbol | Name | Description
1 | VSS | Ground | 0V (GND)
2 | VDD | Power | Power supply for logic circuit and LCD (+4. 5V~+5. 5V)
3 | VEE or VO | Contrast Supply | Bias voltage level to control contrast
4 | RS | Register select | When RS= 1, data register is selected. When RS= 0, instruction register is selected.
5 | RW | Read/Write | When RW= 1, read operation. When RW= 0, write operation.
6 | E | Read Write enable | enable signal to read or write the data
7-10 | DB0-DB3 | Data bus 0-3 | in 8-bit bus mode, used as low order bi-directional data bus. During 4-bit bus mode, open these pins
11-14 | DB4-DB7 | Data bus 4-7 | in 8-bit bus mode, used as high order bi-directional data bus. In case of 4-bit bus mode, used as both high and low order. DB7 used for Busy Flag output

## Slide 5: Contrast and Optional Backlight Information
Optional Pins
  15 A (LED +) Optional: LED Backlight Anode
  16 K (LED -) Optional: LED Backlight Cathode
The optimal contrast for the LCD (VO) is 3.3 - 3.7V, but this may vary with viewing angle, ambient temperature and per-LCD.
Setting the backlight up is optional, but may increase the readability of the LCD and is pretty cool. The backlight on your LCD is one large green LED

## Slide 6: Typical connection
You can verify that your LCD works properly before connecting your LCD data pins.
  Give power to the device and twist the potentiometer one way or the other until you see black lines appear.

## Slide 7: LCD Initialization
The module powers up in 8-bit mode. Additional commands are required to put the module into 4-bit mode
Now we are going to continue using it in 8-bit mode.
<Wait 40us or till BF=0> BF = Busy Flag (D7 of data)
(Two lines LCD with 5×7 matrix) [DB=0x38]
<Wait 40us or till BF=0>
(Display on; cursor on; blink on) [DB=0x0F]
<Wait 40us or till BF=0>
(Clear screen; cursor home) [DB=0x01]
<Wait 1.64ms or till BF=0>
Initialization Complete

## Slide 8: Other useful Commands
[DB=0x06]
  Increment cursor to the right when writing; don’t shift screen
<Wait 40us or till BF=0>
[DB=0x08]
  (Display off; cursor off; blink off)
<Wait 40us or till BF=0>

## Slide 9: MORE LCD COMMANDS
Run sample program:
LCD_Functions_8bit
For more detail see:
LCD_Notes_8-bit.pdf

## Slide 10: LCD 4-bit data mode

## Slide 11
Using LCD in CodeVision

## Slide 12: Initialization
/* the LCD module is connected to PORTC */
#asm
. equ __lcd_port=0x15
#endasm
/* now you can include the LCD Functions */
#include <lcd. h>
Lcd_init(16);

## Slide 13: PORT ADDRESS

## Slide 14: LCD Configuration With CodeWizard

## Slide 15: lcd.h – High Level
unsigned char lcd_init(unsigned char lcd_columns)
void lcd_clear(void)
void lcd_gotoxy(unsigned char x, unsigned char y)
void lcd_putchar(char c)
void lcd_puts(char *str)
void lcd_putsf(char flash *str)

## Slide 16
unsigned char lcd_init(unsigned char lcd_columns)
Example:
lcd_init(16)

## Slide 17
void lcd_clear(void)
صفحه ال سی دی را پاک می کند
void lcd_gotoxy(unsigned char x, unsigned char y)
مکان نما را به سطر و ستون دلخواه می برد
Lcd_gotoxy(4,2)

## Slide 18
void lcd_putchar(char c)
Example :
lcd_putchar('a');
void lcd_putsf(char flash *str)
lcd_putsf(”Hello World");

## Slide 19
void lcd_puts(char *str)
Example:
sprintf(buffer, “tempreture= %d”, temp);
lcd_puts(buffer);

## Slide 20: Example - 7
در سطر اول ستون پنجم كاراكتر ‘a’ و در سطر دوم ستون اول عبارت “CodeVisionAVR” را بر روي يك LCD 2x16 نمايش دهيد.
#include <mega16.h>
#asm
.equ __lcd_port=0x1B ;PORTA
#endasm
#include <lcd.h>
#include <delay.h>
void main(void)
{
lcd_init(16);
while (1)
{
lcd_clear();
lcd_gotoxy(5,0);
lcd_putchar('a');
lcd_gotoxy(0,1);
lcd_putsf("CodeVisionAVR");
delay_ms(200);
};
}

## Slide 21: Example-8
تابعي بنويسيد كه بصورت روان كلمه CodeVision را بر روي LCD نمايش دهد.
#include <mega16.h>
// Alphanumeric LCD Module functions
#asm
.equ __lcd_port=0x1B ;PORTA
#endasm
#include <lcd.h>
#include <delay.h>
void main(void)
{
int i;
lcd_init(16);
while (1)
{
for (i=0;i<7;i++)
{
lcd_clear();
lcd_gotoxy(i,0);
lcd_putsf("CodeVision");
delay_ms(400);
}
};
}

## Slide 22
Keypad

## Slide 23: Keyboard Interfacing
Keyboards are organized in a matrix of rows and columns
  The CPU accesses both rows and columns through ports
    Therefore, with two 8-bit ports, an 8 x 8 matrix of keys can be connected to a microprocessor
  When a key is pressed, a row and a column make a contact
    Otherwise, there is no connection between rows and columns
In IBM PC keyboards, a single microcontroller takes care of hardware and software interfacing

## Slide 24: Scanning and Identifying the Key
A 4x4 matrix connected to two ports
  The rows are connected to an output port and the columns are connected to an input port

## Slide 25: Grounding Rows and Reading Columns
It is the function of the microcontroller to scan the keyboard continuously to detect and identify the key pressed
To detect a pressed key, the microcontroller grounds all rows by providing 0 to the output latch, then it reads the columns
  If the data read from columns is D3 – D0 = 1111, no key has been pressed and the process continues till key press is detected
  If one of the column bits has a zero, this means that a key press has occurred
    For example, if D3 – D0 = 1101, this means that a key in the D1 column has been pressed
    After detecting a key press, microcontroller will go through the process of identifying the key

## Slide 26: Grounding Rows and Reading Columns (cnt’d)
Starting with the top row, the microcontroller grounds it by providing a low to row D0 only
  It reads the columns, if the data read is all 1s, no key in that row is activated and the process is moved to the next row
It grounds the next row, reads the columns, and checks for any zero
  This process continues until the row is identified
After identification of the row in which the key has been pressed
  Find out which column the pressed key belongs to

## Slide 27: Grounding Rows and Reading Columns (cnt’d)
Example: identify the row and column of the pressed key for each of the following.
(a) D3 – D0 = 1110 for the row, D3 – D0 = 1011 for the column
(b) D3 – D0 = 1101 for the row, D3 – D0 = 0111 for the column
Solution :
(a) The row belongs to D0 and the column belongs to D2; therefore, key number 2 was pressed.
(b) The row belongs to D1 and the column belongs to D3; therefore, key number 7 was pressed.

## Slide 30: Run sample code (Keypad)