## Slide 1: Chapter 7 System Compensation (Linear Control System Design)
Instructor: Dr. Cailian Chen

## Slide 2
26/7/29
<number>
Outline
Introduction to compensation design
Phase Lead Compensation
Phase Lag Compensation
Phase Lead-lag Compensation
PID Control

## Slide 3
Given the control plant, the procedure of controller design to satisfy the requirement is called system compensation.
Question: What is system compensation?
Question: Why to compensate?
The closed-loop system has the function of self-tunning. By selecting a particular value of the gain K, some single performance requirement may be met.
Is it possible to meet more than one performance requirement?
Sometimes, it is not possible.
Something new has to be done to the system in order to make it perform as required.

## Slide 4
1.Control system design and compensation
Design：Need to design the whole controller to satisfy the system requirement.
Compensation：Only need to design part of the controller with known structure.
2. Three elements for compensation
Original part of the system
Performance requirement
Compensation device

## Slide 5
1. Time domain criteria（step response）
  Overshoot, settling time, rising time, steady-state error
2. Frequency domain criteria
  Open-loop frequency domain criteria：
  crossover frequency, phase margin, gain margin
  Closed-loop frequency domain criteria ：
  maximum value Mr , resonant frequency, bandwidth
7.1 Introduction to Compensation Design
7.1.1 Performance Requirement

## Slide 6
Frequency domain and time domain criteria
Resonant frequency
Bandwidth
Gain crossover frequency
Phase margin
Resonant peak
Percentage overshoot
Settling time

## Slide 7
According to the way of compensation, the compensator can be classified into following categories:
7.1.2 Structure of Compensator

## Slide 10
Remark：
Cascade compensation and feedback compensation are inside the feedback loop.
Feed-forward compensation and disturbance compensation are outside the feedback loop.

## Slide 11
1. Frequency Response Based Method
  Main idea：By inserting the compensator, the Bode diagram of the original system is altered to achieve performance requirements.
Original open-loop Bode diagram＋Bode diagram of compensator＋alteration of gain
＝open-loop Bode diagram with compensation
7.1.3 Methods for Compensator Design
2. Root Locus Based Method
Main idea: Inserting the compensator introduces new open-loop zeros and poles to change the closed-loop root locus to satisfy the requirement.

## Slide 12
Frequency response based compensation
Phase lead compensation
Phase lag compensation
Phase lead-lag compensation
Fundmantal rule for control design：PID control
7.1.2 Cascade Compensation
Each requirement relates to a different region of the frequency axis in the Bode diagram.
The steady-state error relates to the magnitude at low frequency.
The transient response requirement relates to the gain crossover frequency, which usually occurs at higher frequencies.

## Slide 13
Three design rules for cascade compensator:
The system is stable with satisfactory steady-state error, but dynamic performance is not good enough.
Compensator is used to change medium and high frequency parts to change crossover frequency and phase margin.
The system is stable with satisfactory transient performance, but the steady-state error is large.
Compensator is used to increase gain and change lower frequency part, but keep medium and higher frequency parts unchanged.
3. If the steady-state and transient performance are either unsatisfactory, the compensator should be able to increase gain of the lower frequency part and change the medium and higher frequency parts.

## Slide 14
Change of Bode Diagram
a)change of lower frequency part
b)change of medium and higher frequency parts
b)change of lower, medium and higher frequency parts

## Slide 15
Passive Phase Lead Network
1. Transfer function：
7.2 Phase Lead Compensation
where

## Slide 16
Determination of
Multiplying the transfer function by α
Geometry mean
Notes: <number>

## Slide 17
2、Effect of phase lead compensation

## Slide 18
Example 7.1: Given a unity-feedback system with the following open-loop transfer function
Please design phase lead element to satisfy the following three requirements:
2. phase margin
3. gain margin
1. steady speed error constant

## Slide 19
Uncompensated system
?
Extra margin:
5o~10o

## Slide 20
Remark:
The phase lead compensator not only takes extra phase margin of 33o at the uncompensated gain crossover frequency.
However, we also have to add the magnitude part of the compensator to the uncompensated magnitude, and the gain crossover frequency moves to a higher value. The ultimate phase margin is less than 33o .
It implies we need to consider extra phase margin for determine α.

## Slide 21
Complete Compensator

## Slide 22
Comments on phase lead compensation
1、The slop around the gain crossover frequency is increased. It improves the relative stability.
2、The closed-loop resonance peak is reduced. Also, the overshoot is reduced.
3、Increase the open-loop phase margin.
4、The open-loop (and usually the closed-loop) bandwidths are increased. It is beneficial for fast response. But it may cause problems if noise exists at the higher and unattenuated frequencies.
5、Take no effect on the steady-state performance.

## Slide 23
(4) Determine
(2) Determine the uncompensated phase margin γ0
(7) Confirmation
  (1) Determine K to satisfy steady-state error constraint
(5) Calculate ωm
(6) Determine T
(3) estimate the phase margin in order to satisfy the transient response performance constraint
Rules to design phase lead compensation

## Slide 24
26/7/29
<number>
Constraints for application of lead compensation：
Constraint 1: The system is stable.
If it is unstable, the phase need to compensate is too big. The noise takes severe effects on the system.
Constraint 2: The phase cannot reduce very fast around the gain crossover frequency.
The phase lead compensation can only provide less than 60o extra phase margin.

## Slide 25
Transfer function:
Passive phase lag network
6.3 Phase Lag Compensation

## Slide 26
The compensator has no filtering effect on the low frequency signal, but filters high frequency noise. The smaller β is，the lower the noise frequency where the noise can pass.
Maximum phase lag

## Slide 27
Comments on phase lag compensation:
1、Phase lag compensator is a low-pass filter. It changes the low-frequency part to reduce gain crossover frequency. The phase is of no consequence around the gain crossover frequency.
2、Be able to amplify the magnitude of low-frequency part, and thus reduce the steady-sate error.
3、The slope around gain crossover freuency is -20dB/dec.
Resonance peak is reduced, and the system is more stable.
4、Reduce the gain crossover frequency, and then reduce the bandwidth. The rising time is increased. The system response slows down.

## Slide 28
Rules for phase lag compensator design:
1、Determine K to satisfy the steady-state error；
2、Draw bode diagram for umcompensated system
3、Find the frequency ωc1 from the uncompensated open-loop Bode diagram where the phase margin satisfy the performance requirement；
4、Calculate the magnitude at the frequency ωc1 .
Determine β by
5、Determine the two break frequencies.
6. Comfirmation

## Slide 29
Avoid introduce the maximum phase lag around the gain crossover frequency . So the break frequency is much less than
Substitude
The phase lag at ωc1 is

## Slide 30
0.01
0.1
1
dB

## Slide 31
Example 6.2: Given a unity-feedback controller with the following open-loop transfer function
Please design a cascade compensator to satisfy the following requirements：
Notice: If the compensated system cannot satisfy the requirements, we need to further alter crossover frequency and phase of the lag compensator.

## Slide 32
26/7/29
<number>
Solution:
(1)
(2) Draw the uncompensated Bode diagram
The system is unstable. The needed extra phase compensation is 83.3o . The phase lead compensation can not provide so big phase margin.
Two ways:
Apply two cascade phase lead compensation
Apply phase lag compensation
(3) For ω=2.5 rad/s, γ=45o
Set ωc1=2.5

## Slide 33
26/7/29
<number>
(4) L(ωc1)=22dB
(5)
(6)
Confirmation:

## Slide 34
Applicable for the following systems：
（1）The transient performance is satisfactory, but the steady-state performance is desired to be improved.
（2）High requirement for noise attenuation.
Drawback：The system response is slow down.

## Slide 35
Comparison of phase lead and lag compensation